## Slide 1
Ok, how do I start?
C/C++
First steps with Arduino

## Slide 2
  Getting started with Arduino
    Program installation
    Making Arduino talk to your computer
  The Arduino development environment

## Slide 3
http://arduino.cc/en/Guide/HomePage
Getting started:
  Download the Arduino environment from:
    http://arduino.cc/en/Main/Software
  Install the downloaded file
  Connecting Arduino to your computer
  Install drivers (only if windows requires intervention)
  Connected to the computer; a ‘COM’ port; up to 8 Arduino boards simultaneously.

## Slide 4
Arduino IDE:
  Launch the application
  Select board type and COM#
  Load an example file
  Upload it to the Arduino board
http://arduino.cc/en/Guide/HomePage

## Slide 5: The Arduino development environment
http://arduino.cc/en/Guide/Environment
  Text editor – edit the Sketch
  Massage Box – compiling, uploading, and errors messages
  Toolbar
    Next slide
  Other Information:
    Line number; board type and COM#
    Sketch name; IDE version
text editor
Massage Box
Toolbar

## Slide 6: The Arduino development environment
http://arduino.cc/en/Guide/Environment
Verify Upload New Open Save
Serial monitor

## Slide 7: Programming Learning tools
http://arduino.cc/en/Tutorial/HomePage
http://arduino.cc/en/Reference/HomePage
  Start with example
  Use the reference to understand the code

## Slide 8: Programing
  Blink example
  Code:
GND
D13
220 ohm
LED
Introductive Comments
Declaration of global variables
Setup function
Loop function
Notes: delayMicroseconds()
Minimal is 3 microseconds%

## Slide 9: Programing
/* Blink Turns on an LED on for one second, then off for one second, repeatedly. This example code is in the public domain. */ // Pin 13 has an LED connected on most Arduino boards.
// give it a name: int led = 13;
// the setup routine runs once when you press reset: void setup() { pinMode(led, OUTPUT); // initialize the digital pin as an output. } // the loop routine runs over and over again forever: void loop() { digitalWrite(led, HIGH); // turn the LED on (HIGH is the voltage level) delay(1000); // wait for a second digitalWrite(led, LOW); // turn the LED off by making the voltage LOW delay(1000); // wait for a second }
GND
D13
delayMicroseconds()

## Slide 10: 10 minutes hands-on
Connect Arduino to the computer
Open the IDE
Upload the blink program
Change the blink frequency to 2Hz

## Slide 11: Programing
http://arduino.cc/en/Tutorial/HomePage
http://arduino.cc/en/Reference/HomePage
  Arduino ‘knows’ how to compile C and C++ to AVR
  (AVR = C for Atmel chips)
  Variables require declaration
  Scope: Global, local, Const., Static variables
    Any variable declared outside of a function is Global
    All others are local unless defines as ‘static’.
Notes: A global variable is one that can be seen by every function in a program. Local variables are only visible to the function in which they are declared. In the Arduino environment, any variable declared outside of a function (e.g. setup(), loop(), etc. ), is a global variable.

## Slide 12: Programing
http://arduino.cc/en/Tutorial/HomePage
http://arduino.cc/en/Reference/HomePage
  Data types:
  int speed =400;
  long speedOfLight = 186000;
  Rollover :
  Int Rollover=32767;
  Rollover= Rollover+1;
Rollover now equals -32768
Notes: AVR Code
The Arduino environment is based on Atmel Atmega microcontrollers. The AVR language is a "C" environment for programming Atmel chips. Much of the Arduino language is written with AVR constants and functions and there are many things that are still not easy to accomplish with the Arduino language without using some AVR code.
The good news is that because the Arduino environment uses GCC to compile code, all of the port and register variables found in the Atmega 168 datasheet and tutorials on AVR code assembly language are supported when using the Arduino IDE.
This page is an attempt to document the most useful AVR functions and code snippets.

## Slide 13: Programing
  Other data types:
  char: character value char LetterA=‘a’;
  float : ±3.4028235E+38; 32bits; 6-7 decimal digits of precision
  double: same as float (in Uno)
  Strings:
    char array: char Str[ ] = "arduino";
    Using the ‘String’ library: String text1 =“this is a string”;
  int myPins[] = {2, 4, 8, 3, 6};
    X=myPins[2];
http://arduino.cc/en/Tutorial/HomePage
http://arduino.cc/en/Reference/HomePage
Notes: AVR Code
The Arduino environment is based on Atmel Atmega microcontrollers. The AVR language is a "C" environment for programming Atmel chips. Much of the Arduino language is written with AVR constants and functions and there are many things that are still not easy to accomplish with the Arduino language without using some AVR code.
The good news is that because the Arduino environment uses GCC to compile code, all of the port and register variables found in the Atmega 168 datasheet and tutorials on AVR code assembly language are supported when using the Arduino IDE.
This page is an attempt to document the most useful AVR functions and code snippets.

## Slide 14: Control Structures (if, while, etc.)
http://arduino.cc/en/Reference/If
    If (someVariable>50)
    {
    //do something here;
    }
    For example:
    for (int i=1; i<4;i++)
    {
    Serial.println(i)
    }
x==y
x!=y
X<y
X>y
X<=y
X>=y
while
for
switch/case
do-while
break
return

## Slide 15: Mathematical operations
i=i+1; i++; i+=1
9/4=2;
Modulus: 22%10=2
Abs(-1)=1
min(1,2)=1 (similar for ‘max’)
pow(2,3)=8; sqrt(9)=3
sin(rad); cos(); tan()
sensVal = constrain(sensVal, 10, 150); // limits range of sensor values to between 10 and 150
val = map(val, 0, 1023, 0, 255);
floor;ceil;
PI;RAD_TO_DEG;
random(min,max);
https://www.arduino.cc/en/Reference/Arithmetic
https://www.arduino.cc/en/Reference/HomePage
Notes: long map(long x, long in_min, long in_max, long out_min, long out_max) { return (x - in_min) * (out_max - out_min) / (in_max - in_min) + out_min; }

## Slide 16: Libraries
http://arduino.cc/en/Guide/Libraries
  Collection of code lines
  Built-in libraries
  Others – require installation and to be called at the beginning of the code:
  Import library: > #include <Stepper.h>
Notes: Libraries are a collection of code that makes it easy for you to connect to a sensor, display, module, etc. For example, the built-in LiquidCrystal library makes it easy to talk to character LCD displays. There are hundreds of additional libraries available on the Internet for download. The built-in libraries and some of these additional libraries are listed in the reference. To use the additional libraries, you will need to install them.

## Slide 17: Serial library
  communication between the Arduino board and other deivces (PC over the USB port. Serial sensors) using the serial communication protocol.
  Serial.begin(9600);
  9600 Bits Per Second (baud rate)
  (some) Important procedures:
    begin()
    available()
    print()
    println()
    read()
http://www.ladyada.net/learn/arduino/lesson4.html
See the ‘AnalogReadSerial’ example unber the ‘basic’ category
Notes: Libraries are a collection of code that makes it easy for you to connect to a sensor, display, module, etc. For example, the built-in LiquidCrystal library makes it easy to talk to character LCD displays. There are hundreds of additional libraries available on the Internet for download. The built-in libraries and some of these additional libraries are listed in the reference. To use the additional libraries, you will need to install them.

## Slide 19: Rx and Tx LEDs
10 bits
7-12V
I2C (Inter-Integrated Circuit) and SPI (Serial Peripheral Interface)
Serial communication
Integrated LEDs:
Pin13
TX
RX

## Slide 20: Sensors types
Digital (1 or 0, True or False, High or Low):
Analog: (returning value between 0 and 1023)
Pulse width (e.g. Distance PING)
Serial
Synchronous protocols (I2C, SPI)

## Slide 21: Hands-on #2 Reading an analog sensor (TMP 36)
Safety notes:
Do not short-circuit the I/O pins (Gnd to voltage sources)
Connect devices in the correct polarity
analogRead; Serial.print; delay; Serial.println; if, else logical conditions; Serial.begin

## Slide 22: Hands-on #2 Reading an analog sensor (TMP 36)
analogRead; Serial.print; delay; Serial.println; if, else logical conditions; Serial.begin

## Slide 23
  Program structure
    Define variables
    Establish Serial connection (in the void setup() )
  1.Read analog value:
    Loop: read - sensorValue = analogRead(sensorPin);
    Loop: print - Serial.println(sensorValue);
  Use example named: Basic  readAnalogeVoltage
  2. Convert the ‘analog reading’ to voltage:
  sensorVoltage=map(sensorValue,0,1023,0,5000);
  3. Convert the ‘voltage’ to T(C):
    float sensorTemp =25+(sensorVoltage-750)*.1

## Slide 26: For more that one variable
Plotting the temperature over time:
  Print lines with the variable(s) you want to plot:
Serial.print(sensorTemp2);
Serial.print(“ “);
Serial.println(sensorTemp2);

## Slide 27: Hands-on #3 Reading an analog sensor (TMP 36) and controlling LED
analogRead;
Serial.print; delay; Serial.println; if, else logical conditions; Serial.begin
digitalWrite
analogWrite
LED: short leg to GND via (150-220Ohm) Resistor

## Slide 28
  Program structure:
    As before +
    if (sensorTemp>25){
      digitalWrite(LEDPin,HIGH);
      }
      else{
      digitalWrite(LEDPin,LOW);
      }
  Use example named: Control IfStatementConditional

## Slide 29: Summary
  Getting started with Arduino
    Program installation and making Arduino talk to your computer
  The Arduino development environment
  Libraries
    What are they good for?
    Installation
  Programming

## Slide 30
First steps with Arduino
“OK, how do I start?”
C/C++
?