## Slide 1
Imperial college design collective
Arduino (Genuino) workshop
27-2-2017; 7-3-2017
18:00-20:30
Avi Braun
Notes: Few words about my self:
Physicist; EXSS; IC research fellow.
Arduin since 2013
Arduino workshop
Succesful – pulm treee project;

## Slide 2
Aim
Introduce Arduino to new users: what it is good for, how to start using it, and how to develop your Arduino skills
Learning outcomes – by the end of the workshop you will…
  Understand how Arduino can be used for creative or technological projects, as an educational tool, and in ones research
  Know how to install and connect Arduino to your computer
  Understand how to use the Arduino development environment
  Understand the physical structure and layout of the Arduino
  Be able to program your Arduino to read sensor(s), and to operate actuators according to logical conditions
  Know how to read/send data to your Arduino from your computer
  Be familiar with on-line resources that will allow you to further develop your Arduino skills

## Slide 3
Introduction to Arduino

## Slide 4: Session #1:
Introduction (30 min)
  What is Arduino, and what can you do with it
  Brief history of Arduino
  Arduino (Uno) board overview
  The Arduino ‘family’:
    Shields and modules
    The extended Arduino family
    Likeduinos
  Summary

## Slide 5: What is Arduino?
  (www.arduino.cc)
,Scientists
Arduino is a tool for making computers that can sense and control more of the physical world than your desktop computer.

## Slide 6: What is Arduino?
Microcontroller (Single board)
  Computer: core processor, memory, clock generator, programmable Input/Output peripherals
Internet Of Things

## Slide 7
Arduino monitored High Altitude Balloon

## Slide 8
Speech-Controlled Arduino Robot

## Slide 9
Smart nest
Smart nest

## Slide 10
Home automation
Growduino
3D printers
Robots (autonomous and actively controlled)

## Slide 11: Advantages
Ready and easy to use:
  USB connection
  Power plug
Low cost: starting at $ 9.95 per piece
Open source
  “…people should be able to study our hardware to understand how it works, make changes to it, and share those changes...” (www.arduino.cc)
Accessible:
  A lot of documentation, tutorials for beginners (and experts)
  Modules and shields

## Slide 12: Brief history of Arduino

## Slide 13: Brief history of Arduino
Born in 2005, at the Interaction Design Institute Ivrea, Italy
Massimo Banzi – the challenge: how to teach students to create electronics, fast (and cheap)
  Micronotroller
  Program language
  Development environment
"The philosophy behind Arduino is that if you want to learn electronics, you should be able to learn as you go from day one, instead of starting by learning algebra," David Cuartielles
Democratization of engineering

## Slide 14: Brief history of Arduino
Development environment
  ‘Processing’
Program language
  ‘Wiring’
Microcontroller (the device)

## Slide 15: Brief history of Arduino
open-source (software and hardware)
Interaction Design Institute Ivrea closed at 2010
  Original design files are accessible for free
  Can be used, adapted, changed and redistributed
  Part of Arduino’s DNA:
    New boards, modules, and a free atmosphere of sharing

## Slide 16: Arduino (Uno) Board Overview
10 bits
7-12V
I2C (Inter-Integrated Circuit) and SPI (Serial Peripheral Interface)
Serial communication
Integrated LEDs:
Pin13
TX
RX
5V/3.3 V

## Slide 17: Arduino Board Overview (Uno)
http://arduino-info.wikispaces.com/ArduinoPinCurrent
Arduino I/O pins:
  10 bits with an effective frequency of up to 8000 Hz
  Output of 3.3/5V from digital pins
  Maximum Ratings: DC Current per I/O Pin – 40.0 mA (tested @ 20 mA) DC Current VCC and GND Pins – 200.0 mA 1 VCC pin: can Source a total of 200mA 2 GND pins: can Sink a total of 400mA
  Max data transfer speeds:115kbits(serial); 400kbits (I2C); 4Mbits (SPI)
  https://sites.google.com/site/measuringstuff/the-arduino

## Slide 18: Shields and modules
Adding capabilities to the Arduino board:
  GPS
  SD card
  Real Time Clock
  Displays: LCD, touch screens
  Motors: Servo/DC/Stepper
  Prototype
  Camera
  Joystick
Notes: Microcontroller: avaliable components

## Slide 19: Shields and modules
Adding capabilities to the Arduino board:
  GPS
  SD card
  Real Time Clock
  Displays: LCD, touch screens
  Motors: Servo/Dc/Stepper
  Prototype
  Camera
  Joystick
  Communication:
    Bluetooth
    Cellular: GSM/GPRS and others
    Ethernet/wifi
    Xbee
    RFID
Notes: Microcontroller: avaliable components

## Slide 20: Shields and modules
Sensors and other modules:
  Environment: Temperature, pressure, humidity
  Geiger counter
  Sounds
  Movement: accelometer
  Proximity: ultrasonic/IR/reflection
  Biometric: finger prints/heart pulse
  Light and colors
  Flow
  Force: pressure/bending
  Extended ADC: e.g. 18bits
Notes: Microcontroller: available components

## Slide 21: Meet the greater family

## Slide 22
https://www.arduino.cc/en/Main/Products

## Slide 23
OtherDuinos
http://en.wikipedia.org/wiki/List_of_Arduino_compatibles
Raspberry Pi

## Slide 24: Why Arduino?
Simple, clear programming environment
Open source Extensible: both hardware and software
Inexpensive
Cross-platform – windows, mac OSX, Linux
For scientists:
  Science and engineering education
  Control your experiments environment
  Sensing and measuring experiment
  Data logging
Accessible

## Slide 25
?